## Slide 1: The Dark Side of Operational Wi-Fi Calling Services
Tian Xie1, Guan-Hua Tu1, Chi-Yu Li2, Chunyi Peng, Mi Zhang1
1Michigan State University
2National Chiao Tung University
3 Purdue University

## Slide 2: Wi-Fi Calling Services
Wi-Fi Calling services empower mobile users to access voice and text services over Wi-Fi instead of cellular networks.
All of four U.S. major operators have launched Wi-Fi calling services since 2016 – Verizon, AT&T, T-Mobile, and Sprint.
By 2020, Wi-Fi calling services will take 53% of mobile IP voice service usage including VoLTE (26%) and others (21%).

## Slide 3: Wi-Fi Calling Services Primer
Specifically, they are SIP-based voice and text services, however, they are using a 3GPP-modified version.
  Developed on top of 3GPP IMS (IP Multimedia Subsystem)
    Operators use IMS to provide users with IP-based services such as VoIP
  It uses the same infrastructure for VoLTE (Voice over LTE) users.
Radio Access Network (RAN)
  Wi-Fi Access Point (Wi-Fi Calling)
  eNodeB (VoLTE)
LTE Core Network (CN)
  ePDG (Evolved Packet Data Gateway, Wi-Fi calling)
  PDN-GW (Public Data Network Gateway)
  AAA (Authentication, Authorization, and Accounting)
  IMS (IP Multimedia Subsystem)

## Slide 4: Wi-Fi Calling Security Mechanisms
Using well-examined 3GPP Authentication and Key Agreement (AKA) and SIM-based security adopted by VoLTE – symmetric cryptography.
How Does It Go Wrong?
All Wi-Fi calling signaling and voice/text packets are delivered through IPsec (Internet Protocol Security) – ciphering and integrity protection.

## Slide 5: Finding 1: Wi-Fi calling devices will activate Wi-Fi calling services over an insecure Wi-Fi network

## Slide 6: Vulnerability: Wi-Fi calling devices do not exclude insecure Wi-Fi networks – (design defect of standards)
Vulnerability – Wi-Fi calling standards don’t exclude insecure Wi-Fi
  Two Wi-Fi access point selection modes do not consider security factors yet!!
  Manual (use a prioritized list)
  Automated (ANDSF, Access network discovery and selection function)
All tested Wi-Fi calling devices connected to the insecure Wi-Fi router!!!
Validation:
  Deploy an insecure Wi-Fi network using a Wi-Fi router which is vulnerable to ARP spoofing attack – foundation of a variety of MITM attacks
    I.e., victim’s WIFI packets will be intercepted and delivered to adversaries
  We test whether the Wi-Fi calling devices keep connecting to the above Wi-Fi router

## Slide 7: Finding 2: Wi-Fi calling devices do not employ security defense against the common Wi-Fi ARP spoofing attacks

## Slide 8: Vulnerability: Wi-Fi calling devices do not defend against ARP spoofing attacks –(implementation issue of devices)
Vulnerability -Wi-Fi calling devices always accept ARP Reply message
  All packets sent by Wi-Fi calling devices can be redirected to adversaries
Validation
  We use EtterCap to send ARP reply message to Wi-Fi calling devices.
Adversaries can capture all Wi-Fi packets sent by the victim

## Slide 9: Finding 3: Wi-Fi calling devices and infrastructure indeed deploy extra security mechanisms for malicious Wi-Fi attacks, however, it is not enough.

## Slide 10: A system-switch mechanism for Wi-Fi Calling Service DoS Attacks
With the aforementioned two findings, adversaries can launch Wi-Fi Calling service DoS attacks
  Discarding all intercepted Wi-Fi signaling and voice/text packets
System-switch (Wi-Fi-> Cellular)
  If an user fails to dial a Wi-Fi voice call, the mobile device will switch to use cellular-network-based voice services.
  If Wi-Fi calling service operators cannot route an incoming call to users by Wi-Fi calling, the operators will switch it to use cellular-network-based one.
For users, they are free of voice/text DoS attacks.

## Slide 11: Vulnerability: Service continuity is not revised accordingly – (design defect of standards)
Service continuity can seamlessly switch an ongoing Wi-Fi calling call to back to cellular-network-based voice call
However, it is only triggered while the quality of Wi-Fi radio signals is bad
We start dropping all Wi-Fi calling packets after the call conversation is started (Wi-Fi radio quality is good)
What if Wi-Fi radio quality is good but Wi-Fi calling service quality is poor?
The system-switch security mechanism is bypassed!!
No cellular-based voice call is initiated.

## Slide 12: Finding 4: Wi-Fi calling service operators do not take extra security mechanisms to protect the encrypted Wi-Fi calling packets

## Slide 13: Vulnerability : The Wi-Fi calling traffic is vulnerable to side-channel attacks – (operational slip of operator)
Vulnerability -Wi-Fi calling is the only service that is carried by the IPSec channel between the mobile device and ePDG.
Validation
  Apply C4.5 to analyze IPSec traffic patterns
  We are able to infer six Wi-Fi calling events
    Evt I: Activating Wi-Fi calling service
    Evt II: Receiving an incoming call
    Evt III: Dialing an outgoing call
    Evt IV: Sending a text
    Evt V: Receiving a text
    Evt VI: Deactivating Wi-Fi calling service
  Adversaries may infer various Wi-Fi calling events such as dialing calls, receiving calls, etc.

## Slide 14: Two Proof-of-concept Attacks

## Slide 15: Attack 1: User privacy leakage
The call statistics has been proven effective to infer user privacy including personality[1], mood[2], malicious behaviors[3], etc.
[1] Y.-A. de Montjoye, J. Quoidbach, F. Robic, and A. S. Pentland, “Predicting personality using novel mobile phone-based metrics,” in International conference on social computing, behavioral-cultural modeling, and prediction. Springer, 2013
[2] S. Thomee, A. H ´ arenstam, and M. Hagberg, “Mobile phone use and ¨ stress, sleep disturbances, and symptoms of depression among young adults-a prospective cohort study,” BMC public health, vol. 11, no. 1, p. 66, 2011.
[3] V. Balasubramaniyan, M. Ahamad, and H. Park, “Callrank: Combating SPIT using call duration, social networks and global reputation,” in CEAS’07, 2007
Devising WiCA (Wi-Fi Calling Analyzer) to infer a Wi-Fi calling user’s call statistics
  Who initiates the call (an incoming call or an outgoing call)
  Who hangs up the call first (caller or callee)
  Ringing time (how long the callee answers the call)
  Call conversation time

## Slide 16: Infer call statistics@WiCA
WiCA’s finite state machine
  Record the number of Uplink and Downlink packets transmitted every 2 seconds
  Classify them into three categories by packet size:
    Small (<200 bytes), Medium(200-800 bytes), Large (>800 bytes)
Our observations on small packets

## Slide 17: Ringing time inference
We observe that Wi-Fi calling service servers will keep sending small packets to both of caller and callee after SIP RINGING message is sent by the callee.
Packet arrivals for the event ‘receiving a call with a ringtone’ (callee perspective).
Packets sent by Wi-Fi calling server
Packets sent by the callee
Small downlink packets can be used to detect Ringing
No uplink small packets after callee’s phone is ringed

## Slide 18: Conversation time inference
Packet arrivals for ‘Talking’ (callee perspective).
Packets sent by Wi-Fi calling server
Packets sent by the callee
We observe small packets on the uplink and downlink during the call conversation

## Slide 19: Call initiation and termination inference
Relying on the directions and patterns of large packets
  E.g., if the ringing or talking event is detected and the first large packet (SIP INVITE) is sent by the monitored Wi-Fi user => It is an outgoing call
  E.g., if the talking and not-talking events are detected and the last large packet (200 OK) is sent by the Wi-Fi server => the monitored Wi-Fi user terminates call first

## Slide 20: Performance of WiCA
Who initiates, Who ends call first : 100% accurate
Ringing time and conversation time
  Maximum error is less than 0.8 seconds.

## Slide 21: Another application of WiCA
By face recognition, It is not difficult to identify who you are
How about their IP addresses if they are using free public WiFi?
Xie
Tu
Peng
Li
Mi
Xie?
Peng?

## Slide 22: WiCA with visual recognition system
With the mature visual recognition system, WiCA’s call statistics can help to identify both of user identities and their IP addresses
The ways people are surfing and talking on phones are different
We know which of IP addresses is to initiate Wi-Fi calling call and its call statistics.

## Slide 23: Attack 2: Telephony harassment or denial of voice service attack (THDoS)
We devise a telephony harassment or denial of voice service attack against Wi-Fi calling users.
  It can bypass the security defenses deployed on Wi-Fi calling devices and the infrastructure.
  The attack is based on the manipulation of the delivery of Wi-Fi calling signaling and voice packets for an ongoing call.
  It contains several variants.

## Slide 24: Results of Discarding Wi-Fi Signaling and Voice packets
Wi-Fi calling Call Flow

## Slide 25: Four Call Attack Variants
Attack Wi-Fi signalings
  Annoying-Incoming-Call Attack – keep receiving calls
    Caller will be forced to get stuck in the dialing screen without any altering tone
    Discarding 180 Ringing message
  Zombie-Call Attack – a call cannot be ended
    The caller’s device gets stuck in the dialing screen and will keep hearing the altering tone without starting the conversation.
    Discarding 200 OK message

## Slide 26: Four Call Attack Variants (cont.)
Attack Wi-Fi voice packets
  Mute Call Attack – a muted call
    Can only mute a call for 8s, call will be terminated by network
    Not terminate the call but only mute the call
  Telephony Denial-of-Voice-Service Attack
    Can make the conversation be hardly continued

## Slide 27: Real-world Impact
We find that Wi-Fi calling users will suffer from the devised proof-of-concept attacks, specifically for the users who are using campus Wi-Fi
  Usually provide their faculty, staff, students, and guests with free Wi-Fi
  However, they are not always secure (cannot defend against our attacks)
    MSU
    New York University
    University of California Berkeley
    Northeastern University
    etc

## Slide 28: Solutions
Notes: First, we’ll introduce the vulnerabilities we found under each question.

## Slide 29: Solutions
Short-term: Using Virtual Private Network (VPN) service
  It aims to increase the difficulty of launching side-channel attacks
  Adversaries cannot easily infer each Wi-Fi calling service signalings/voice/text packets
Long-term: Revisit Wi-Fi calling service standards
  Stipulate required security mechanisms which defends against the state-of-the-art Wi-Fi based attacks
  Empower both Wi-Fi calling device and infrastructure to detect whether users are under the attack by monitoring the quality of Wi-Fi calling services and take actions (e.g., excluding malicious Wi-Fi networks)
  Revise the current service continuity procedure from security perspective

## Slide 30: Conclusion
We conducted the first security study on exploring the dark side of operational Wi-Fi calling services provided by three major U.S. operators as well as their commodity Wi-Fi calling devices.
Four security vulnerabilities are discovered, which stem from design defects of Wi-Fi calling standards, operational slips of operators, and implementation issues of Wi-Fi calling devices.
We demonstrate the negative real-world impacts (e.g., WiFi DoS) by two proof-of-concept attacks and provide recommended remedies.
Our lessons learned can secure both Wi-Fi calling service users and operators and facilitate its global deployment, as well as provide new design insights for upcoming 5G networks.

## Slide 31
Thank you! Questions?

## Slide 32: Backup